Running KM in amazon EC2

Preliminary checks on aws on (m5.large m5n.large t2.large) different instances show EC2 does not expose VMX functionality. The instances selected are the latest generation or one generation behind latest generation Intel processors.

Current KM needs

For running KM we need less than full featured hypervisor. Some are features essential

- Having a separate address space when running payload code.
  - When running payload no kernel memory should be mapped.
  - When running KM mode address map looks like a regular process with guest memory mapped to KM address space.

- Switch to payload mode.
  - In payload mode no access any system services.
  - System calls use a sanitized exit tunnel KM provides.

- Switch back to monitor mode.
  - All system services should be available.
  - Read and Write access to payload memory.

- Special instructions executed by kernel on behalf of payload code.
  - Currently KM uses “OUT” instruction for system services.

- Fault handling.
  - Illegal instructions
  - page faults
  - privileged instructions
  - interrupts
  - timer service.
  - Additional exceptions need proper forwarding to kernel/KM on a per instance basis.

- IO services
  - We don’t currently allow IO/Network services as part of payload. All services are provided by KM.

- Isolation
  - Other guests and hypervisor are protected from payload.

KVM functionality currently being used

- Physical memory management.
  - KVM currently allows for creating and mapping guest memory to KM space.
  - Further management of this is done in KM code.

- Virtual CPU creation and scheduling.
  - We are creating a new VCPU per pthread. Scheduling of these VCPUS and binding them to physical CPUS is done by KVM.

- Library/System call/fault
  - Exit from guest mode to KM mode is provided by KVM.(OUT instruction)

- Debug support.
  - Debug trap exit from payload mode back to KM mode and forwarding is done by KVM.

KVM is providing a ‘Kontain virtual system’ and binding it with memory and CPUS dynamically.

Amazon disabled VMX functionality for EC2 instances, so nested virtualization does not work. VMCS functionality is disabled.

KVM currently uses VMCS hardware support to

- enter and exit payload mode
- switching EPT and page table management
- exit on fault
- emulate privileged instructions

 How to implement nested virtualization on EC2

Intuitive easy approach.

Run another layer of virtualization like below

EC2 Hypervisor
Some Linux + ISA emulator
Hardware
Kontain OS + KVM
Guest
KM

Guest
KM

This above implementation is quick. Has substantial overhead due to extra layer of operating system and ISA emulator. Further the payload is completely emulated.

Second approach.

Emulate the needed features that are lacking for a regular process running on a OS.
EC2
Hardware
Kontain OS + Kontain PAS
Guest
KM

Guest
KM

Emulate missing functionality provided by VMCS by either adding a new module or modify KVM to stop using unsupported functionality in EC2.

When a new instance of KM is started create process with default address space and payload address space(PAS). The PAS is similar to a guest address space with tweaks

- Payload runs at RING 3 privilege.
- Implement hooks to capture async events generated by hardware in RING 0 code.
- PAS RING 0 code will be able to switch back to normal kernel mode.
  - context to switch back to kernel has to be tracked as part of PAS.
  - If a malicious RING3 code manages to modify RING 0 memory in PAS context the operating system will not be able to recover.
- Implement sanity checks as part of switch from PAS to happens.

Jail proposed using context switch is not as good as the one provided by VMX hardware. Malicious guest can take down the complete environment.

VMX jail is much safer than the above proposal. The switch and switch back context(VMCS) is tracked in hardware. Hardware does all the heavy lifting by isolating hypervisor memory from malicious guest.